## Slide 1: PS-028
Happy Eyeballs IPv4/IPv6 Fallback Measurement
Faculty Mentor: Prachi Sharma
Students: Roshni Singh & Shruti Kumari

## Slide 2: Problem Description
Dual-stack clients often meet broken or slow IPv6 paths while IPv4 works fine.
1
The Connection Delay Trap
20+ sec
TCP timeout before IPv4 fallback
Without a fallback mechanism, a client using a failing IPv6 route waits for a full TCP timeout before trying IPv4.
2
The Measurement Gap
No data
granular, real-time fallback telemetry
Operators lack visibility into how often clients fall back, why, and the exact penalty of fixed connection-delay timers.

## Slide 3: Background
Client
DNS
Resolution
A record (IPv4)
AAAA record (IPv6)
Dual-stack
Server
✗ may be dropped (carrier, router, tunnel)
IPv6 preferred
OS and browsers choose IPv6 for its architectural advantages.
Paths can break
Carrier networks, misconfigured home routers and tunnel failures drop IPv6.
Why measure
Fallback measurement is critical for performance tuning.

## Slide 4: Literature & RFC Review
RFC 6555
Happy Eyeballs v1 [1]
Parallel attempts with a small delay: prefer IPv6, swift fallback.
RFC 8305
Happy Eyeballs v2 [2]
Better address sorting, concurrent DNS lookups, standard delay timers.
Studies
APNIC & RIPE Labs [4][6]
Fixed 250–300 ms timers penalize high-latency links.
Chart: 
| IPv6 success | Other
IPv6 | 90 | 10
>90%
native IPv6 success
Takeaway: IPv6 mostly works, yet static timers still hurt slower links. The gap: no fine-grained, real-time fallback telemetry or adaptive delay. Also see RFC 6556 [3], [5].

## Slide 5: Proposed Solution
Active-Passive Hybrid Telemetry Framework: capture, aggregate and analyze IPv4/IPv6 fallback metrics across client apps.
Client Application
+
Lightweight Telemetry Probe
1
DNS resolution times
2
TCP handshake times (IPv4 & IPv6)
3
Network metadata: ASN, geo-location

## Slide 6: Optimization Proposed
ADDT: Tdelay = max(min_threshold, α × RTTavg)
Fixed timer
IPv6 wait: 250–300 ms
IPv4 starts early
Adaptive (ADDT)
IPv6 wait: α × RTTavg (high-latency link)
IPv4 starts
Time →
Scenario | Before (static timer) | After (ADDT)
High-latency links | Premature fallback to IPv4 | Premature fallback prevented
Rapid recovery | Preserved | Preserved (min_threshold floor)
Delay adjustment | Fixed, one value for all | Local historical RTT based

## Slide 7: Solution Architecture & Design
1
Client Probe SDK
Intercepts connection races, logs handshake durations, captures fallback triggers.
2
Ingestion Gateway
High-throughput API endpoint (gRPC/HTTPS) ingesting telemetry payloads.
3
Time-Series Storage
Prometheus/InfluxDB backend optimized for high-frequency metrics.
Probe SDK → Ingestion Gateway → Time-Series Storage → Analytics Dashboard

## Slide 8: Data Flow Diagram
Client
Application
Ingestion
Gateway
TSDB
Analytics
Dashboard
DNS & parallel race (IPv4 / IPv6)
telemetry payloads (gRPC/HTTPS)
high-frequency metrics
queries & insights
Fallback triggers, handshake times and ASN/geo metadata flow end to end for analysis.

## Slide 9: Deployment Timeline
1
Weeks 1–3
Finalize SDK specifications and define event schemas
2
Weeks 4–6
Internal pilot, staging integration, simulation testing
3
Weeks 7–9
Staged production rollout to 10% live user base
4
Weeks 10–12
General availability, dashboard calibration, ADDT tuning

## Slide 10: Bibliography
1
D. Wing, A. Yourtchenko. “Happy Eyeballs: Success with Dual-Stack Hosts.” RFC 6555, IETF, 2012.
2
D. Schinazi, T. Pauly. “Happy Eyeballs Version 2: Better Connectivity Using Concurrency.” RFC 8305, IETF, 2017.
3
F. Baker. “Testing Eyeball Happiness.” RFC 6556, IETF, 2012.
4
V. Bajpai, J. Schönwälder. “Measuring the Effects of Happy Eyeballs.” ANRW ’16, 2016. doi:10.1145/2959424.2959429
5
V. Bajpai, J. Schönwälder. “IPv4 versus IPv6 – who connects faster?” IFIP Networking, 2015. doi:10.1109/IFIPNetworking.2015.7145323
6
P. Sattler et al. “Lazy Eye Inspection: Capturing the State of Happy Eyeballs Implementations.” ACM IMC ’25, 2025. doi:10.1145/3730567.3732925

## Slide 11: Thank You for Your Attention!
Questions?